SS800 Revised 08/11/10

614.03

On page 472, Add the following paragraphs after the eighth paragraph of the section:

Ensure that all project motor vehicles and trailers as set forth in ORC 4511.01, including project delivery motor vehicles, comply with the motor vehicle operating, lighting, and delineation requirements of ORC 4513.11, ORC 4513.17, and as set forth herein.

Equip all project motor vehicles with photo strobe lights, LED warning lights, or rotating beacons meeting Class 1 or Class 2 specifications for color and intensity as defined by the Society of Automotive Engineers (SAE).

Photo strobe lights, LED warning lights, or rotating beacons shall be horizontally visible from all directions (360 degrees) at a distance of 100 feet minimum. In order to ensure this visibility, the light shall in no way be obstructed from view by any signs or appurtenances on the motor vehicle.

Activate the photo strobe lights, LED warning lights, or rotating beacons and all hazard lights anytime the motor vehicle is entering, exiting or operating in a traveled lane at a speed less than the posted speed within the limits of the work zone or one mile of either end of the work zone.

In addition, equip all project motor vehicles and trailers having a gross motor vehicle weight rating of 10,000 pounds or greater, in single or combination, with conspicuity tape.  Also, delineate all NCHRP 350 Category IV equipment (lighted arrows, changeable message signs, etc.) with conspicuity tape.

Conspicuity Tape:  Use red and white, Type G, H, or J retroreflective sheeting that complies with 730.19, 730.192, and 730.193.

a.	Apply one 2-inch wide (minimum) horizontal stripe of Type G, H, or J retroreflective sheeting to a minimum of 50 percent of the length of each side of the payload portion of the motor vehicle, rearward from the back of the cab, NCHRP 350 Category IV equipment, and trailers. Space lengths of tape evenly over the length of the payload portion of the motor vehicle rearward from the back of the cab, NCHRP 350 Category IV equipment, and trailers. The centerline for each strip of retroreflective sheeting shall be between 15 inches and 60 inches above the road surface when measured with the motor vehicle empty or unladen, or as close as practicable to this area.

b.	Outline the lower rear facing area of the motor vehicle, NCHRP 350 Category IV equipment, and trailers with 2-inch wide (minimum) horizontal stripe of Type G, H, or J retroreflective sheeting. Apply the lower horizontal markings extending the width of the motor vehicle, NCHRP 350 Category IV equipment, and trailer as close as practical to the edge of the motor vehicle, NCHRP 350 Category IV equipment, and trailer.  The centerline for each strip of lower horizontal retroreflective sheeting shall be between 15 inches and 72 inches above the road surface when measured with the motor vehicle empty or unladen, or as close as practicable to this area.

c.	Outline the upper rear facing area with two pairs of strips of 2-inch wide (minimum) retroreflective Type G, H, or J sheeting, each pair consisting of strips 12 inches long, must be positioned horizontally and vertically on the right and left upper corners of the rear of the body of each motor vehicle or trailer, as close as practicable to the top of the motor vehicle or trailer and as far apart as practicable. If the perimeter of the body, as viewed from the rear, is not square or rectangular, the strips may be applied along the perimeter, as close as practicable to the uppermost and outermost areas of the rear of the motor vehicle or trailer on the left and right sides.

Escort transport or delivery motor vehicles without proper photo strobe lights, LED warning lights, or rotating beacons or conspicuity tape to and from the work zone only with the approval of the Engineer.  This exception is intended for limited use at the discretion of the Engineer and will only be considered following a written request by the contractor.  Otherwise, equip all project motor vehicles with photo strobe lights, LED warning lights, or rotating beacons and conspicuity tape as described herein.

Equip all project motor vehicles with photo strobe lights, LED warning lights, or rotating beacons and conspicuity tape as set forth in this section no later than October 1, 2010.

Equip all project motor vehicles with photo strobe lights, LED warning lights, or rotating beacons meeting Class 1 specifications for color and intensity as defined by the Society of Automotive Engineers (SAE) no later than January 1, 2012.